## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 2: x86 Processor Architecture
(c) Pearson Education, 2010. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 2/15/2010
Kip Irvine

## Slide 2: Basic Microcomputer Design
Central Processor Unit:
  clock synchronizes CPU operations
  control unit (CU) coordinates sequence of execution steps
  ALU performs arithmetic and logic operations
Bus: transfer data between different parts of the computer
  Data bus, Control bus, and Address bus

## Slide 3: Clock
synchronizes all CPU and BUS operations
clock cycle measures time of a single operation
clock is used to trigger events
Clock cycle duration = 1/(clock speed in Hz)
  Ex: if speed is 1GHz then duration = 1 nanosecond
Instruction execution: between 1 to 50+ clock cycles.

## Slide 4: Instruction Execution Cycle [Fetch-and-Execute Cycle]
Loop:
  Fetch next instruction then increment IP (the Instruction Pointer)
  Decode the instruction
  If memory operand needed then
    Fetch operand’s value from memory
  Execute the instruction
  If result is memory operand then
    Store output to memory
Continue loop

## Slide 5: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
(See Page 27)
Instruction Execution Cycle

## Slide 6: The Platform We Will Use
Assembly language and machine language are processor specific
  We will write code for Intel’s 80x86 (x>=3)
  IA-32 family: Intel 80386, 486, … Pentium, …
The assembler places its machine code into an object file which is OS specific
  Our code will run (only) on Windows
    And it will crash on DOS
  Our programs will be Win32 console applications
    These are programs for which all I/O operations are character-based
    They run into an MS-DOS box but they are not DOS programs (they do not use DOS calls)

## Slide 7: The Intel X86 Family
The instruction set of the x86 is backward compatible with any one of its predecessors
  New additional instructions are introduced with each new processor
8086
80286
80386
80486
Pentium
. . .

## Slide 8: Basic Program Execution Registers
Registers: high-speed memories located in the CPU
Registers for 8086 and 80286 are 16 bits wide
Registers for IA-32 family are 32 bits wide

## Slide 9: General-Purpose Registers
8 registers used for arithmetic and data movement
  Use 8-bit name, 16-bit name, or 32-bit name
  Applies to EAX, EBX, ECX, and EDX only

## Slide 10: Index and Base Registers
Some registers have only a 16-bit name for their lower half:
EBP/ESP registers are used as pointers to stack
ESI/EDI registers used for fast memory indexing.

## Slide 11: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment:
    stores the address of a memory segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 12: Segment Registers
Each program is subdivided into logical parts called SEGMENTS
  Code segment (CS)
  Stack segment (SS)
  Data segments (DS, ES, FS, and GS)
Real-address mode: segment registers hold the “base address” of these program segments
Protected mode: segment registers hold pointers to segment descriptor table
Segment registers are 16-bit wide
CS
SS
DS
ES
FS
GS

## Slide 13: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
  Stores the address of the next instruction to be executed
  IP for 8086
EFLAGS
  control flags:
    Controling the operation of the CPU
  status flags:
    Reflecting outcome of CPU operations
  each flag is a single binary bit
    Set flag = 1 and Clear flag = 0

## Slide 14: EFLAGS’s Status Flags
Carry
  CF: unsigned arithmetic out of range
Overflow
  OF: signed arithmetic out of range
Sign
  SF: result is negative
Zero
  ZF: result is zero
Auxiliary Carry
  AF: carry from bit 3 to bit 4
Parity
  PF: sum of 1 bits is an even number
Direction DF: (CPU control flag)
  Process arrays up or down ?

## Slide 15: Floating-Point UNIT, MMX, XMM Registers
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations
Skip to Page 23

## Slide 16: Early Intel Microprocessors
Intel 8080
  64K addressable RAM
  8-bit registers
  CP/M operating system
  S-100 BUS architecture
  8-inch floppy disks!
Intel 8086/8088
  IBM-PC Used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)

## Slide 17: The IBM-AT
Intel 80286
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  80287 floating point unit

## Slide 18: Intel IA-32 Family
Intel386
  4 GB addressable RAM, 32-bit registers, paging (virtual memory)
Intel486
  instruction pipelining
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 19: 64-bit Processors
Intel64
  64-bit linear address space
  Intel: Pentium Extreme, Xeon, Celeron D, Pendium D, Core 2, and Core i7
IA-32e Mode
  Compatibility mode for legacy 16- and 32-bit applications
  64-bit Mode uses 64-bit addresses and operands

## Slide 20: Intel Technologies
HyperThreading technology
  two tasks execute on a single processor at the same time
Dual Core processing
  multiple processor cores in the same IC package
  each processor has its own resources and communication path with the bus

## Slide 21: Intel Processor Families
Currently Used:
Pentium & Celeron – dual core
Core 2 Duo - 2 processor cores
Core 2 Quad - 4 processor cores
Core i7 – 4 processor cores

## Slide 22: CISC and RISC
CISC – complex instruction set
  large instruction set
  high-level operations
  requires microcode interpreter
  examples: Intel 80x86 family
RISC – reduced instruction set
  simple, atomic instructions
  small instruction set
  directly executed by hardware
  examples:
    ARM (Advanced RISC Machines)
    DEC Alpha (now Compaq)

## Slide 23: Logical and Physical Addresses
Addresses specify the location of instructions and data
Addresses that specify an absolute location in main memory are physical addresses (called linear addresses)
  They appear on the address bus
Addresses that specify a location relative to a point in the program are logical (or virtual) addresses
  They are addresses used in the code and are independent of the structure of main memory
Each logical address for the x86 consist of 2 parts:
  A segment number used to specify a (logical) part of the program [The physical address of the segment]
  A offset number used to specify a location relative to the beginning of the segment

## Slide 24: Segmented Memory
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment

## Slide 25: IA-32 Processor Architecture (Modes of Operation)
Protected mode: programs in separate segments
  native mode (Windows, Linux)
  Supported by all x86 except 8086
Real-address mode: 8086
  native MS-DOS
  Supported by all x86
System management mode: customized processor
  power management, system security, diagnostics
Virtual-8086 mode
  Protected, but can execute real-address mode software
  each program has its own 8086 computer

## Slide 26: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 27: Address Translation and Running Modes
The translation from logical to physical addresses is done at run time
The way in which this address translation is done depends on the running mode of the x86
Two different running modes exist for the x86:
  Real mode (supported by every x86)
  Protected mode (all x86 except the 8086)
    You will use this mode

## Slide 28: IA-32 Memory Management (Real-Address mode)
1 MB RAM maximum addressable
Application programs can access any area of memory
Single tasking
Supported by MS-DOS operating system

## Slide 29: Address Translation in Real Mode
The 16-bit segment number (contained in a segment register) is first multiplied by 16 to give the 20-bit physical address of the first byte of the referenced segment: Seg_adr + Off_adr
Then we add the 16-bit offset address to obtain the 20-bit physical address of the referenced data (or instruction)
  Ex: if CS contains 15A6h (in hexadecimal), and IP contains 0012h, then
    The physical address of the instruction to be executed next is just 15A60h + 0012h = 15A72h

## Slide 30: Calculating Linear Addresses
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0

## Slide 31: Your turn . . .
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.

## Slide 32: Your turn . . .
What segment addresses correspond to the linear address 28F30h?
Many different segment-offset addresses can produce the linear address 28F30h. For example:
28F0:0030, 28F3:0000, 28B0:0430, . . .

## Slide 33: Characteristics of (Archaic) Real Mode
Can address only up to 1MB of physical memory
  Uses 20-bit address for referenced segment
Does not support multitasking
  Only 1 process at a time is active
No protection is provided: a program can write anywhere (and corrupt the operating system)
The 8086 runs only in this mode
DOS is a real-mode operating system
Our programs will not run in this archaic mode
  They will run in protected mode which does not suffer from any of these limitations

## Slide 34: IA-32 Memory Management (Protected Mode)
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows

## Slide 35: Protected mode
Segment descriptor tables
Program structure
  code, data, and stack areas
  CS, DS, SS segment descriptors
  global descriptor table (GDT)
MASM Programs use the Microsoft flat memory model

## Slide 36: Address Translation in Protected Mode
The logical/virtual address of a referenced word is given by a pair of numbers (segment, offset)
The segment number is contained in a segment register and is used to select (or index) an entry in a segment table (called a descriptor table)
  Hence, a segment register is also called a selector
The selected entry (the descriptor) contains the base address and length of the referenced segment
The 32-bit base address is added to the 32-bit offset to form a 32-bit linear address (P1,P2,D)
  P1 indexes a directory page table (in memory) to obtain the base address of a second page table which is indexed by P2 to give the physical address of the referenced word

## Slide 37: Intel 386 Address Translation
P1
P2
D

## Slide 38: The FLAT Memory Model
The segmentation part is hidden to the programmer when the base address of each segment descriptor is the same
  Each selector then points to the same segment so that code, data, and stack share the same segment
  Protection bits (read-only, read-write) in each descriptor can still be used
  Done by Windows, Linux, FreeBSD…
The offset part of the logical address is then equivalent to the linear address (P1,P2,D).
  Only the offset part of the logical address is used to specify the location of a referenced word
  The address space is then said to be FLAT
  All our programs will use the FLAT memory model

## Slide 39: Flat Segment Model
Single global descriptor table (GDT).
All segments mapped to entire 32-bit address space
Skip the remaining pages

## Slide 40: Multi-Segment Model
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program

## Slide 41: Paging
Supported directly by the CPU
Divides each segment into 4096-byte blocks called pages
Sum of all programs can be larger than physical memory
Part of running program is in memory, part is on disk
Virtual memory manager (VMM) – OS utility that manages the loading and unloading of pages
Page fault – issued by CPU when a page must be loaded from disk

## Slide 42: 54 68 65 20 45 6E 64
What do these numbers represent?

## Slide 43: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 44: Intel 965 Express Chipset

## Slide 45: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 46: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 47: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 48: 42 69 6E 61 72 79
What does this say?