## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 7: Integer Arithmetic
(c) Pearson Education, 2010. All rights reserved. You may modify and copy this slide show for your personal use, or for use in the classroom, as long as this copyright statement, the author's name, and the title are not changed.
Slides prepared by the author
Revision date: 2/15/2010
Kip R. Irvine

## Slide 2: Integer Multiplication
Contrary to addition, the multiplication operation depends on the interpretation:
  no interpretation: FFh x 2h = ??
  unsigned interp.: 255 x 2 = 510
  signed interpret.: -1 x 2 = -2
We thus have two different multiplication instructions:
    MUL source ;for unsigned multiplication
    IMUL source ;for signed multiplication
Where source must be either mem or reg
  Source is the “multiplier” and the “multiplicand” is in an A_ register

## Slide 3: MUL Instruction
The MUL (unsigned multiply) instruction multiplies an 8-, 16-, or 32-bit operand by either AL, AX, or EAX.
The instruction formats are:
    MUL r/m8
    MUL r/m16
    MUL r/m32
Hence, there is always enough space to hold the result (the product)
  Size of Result is always twice larger as Source and Multiplicand

## Slide 4: MUL Examples
100h * 2000h, using 16-bit operands:
.data
val1 WORD 2000h
val2 WORD 100h
.code
mov ax,val1
mul val2 ; DX:AX = 00200000h, CF=1
CF=1 if and only if the product cannot be contained within the least significant half (lsh) of its storage location
The Carry flag indicates whether or not the upper half of the product contains significant digits.
mov eax,12345h
mov ebx,1000h
mul ebx ; EDX:EAX = 0000000012345000h, CF=0
12345h * 1000h, using 32-bit operands:

## Slide 5: Your turn . . .
mov ax,1234h
mov bx,100h
mul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = 0012h, AX = 3400h, CF = 1

## Slide 6: Your turn . . .
mov eax,00128765h
mov ecx,10000h
mul ecx
What will be the hexadecimal values of EDX, EAX, and the Carry flag after the following instructions execute?
EDX = 00000012h, EAX = 87650000h, CF = 1

## Slide 7: IMUL Instruction
IMUL (signed integer multiply ) multiplies an 8-, 16-, or 32-bit signed operand by either AL, AX, or EAX
Preserves the sign of the product by sign-extending it into the upper half of the destination register
Example: multiply 48 * 4, using 8-bit operands:
mov al,48
mov bl,4
imul bl ; AX = 00C0h, OF=1
OF=1 because AH is not a sign extension of AL.
OF=1 if and only if the product cannot be contained within the least significant half (lsh) of its storage location

## Slide 8: IMUL Examples
Multiply 4,823,424 * -423:
mov eax,4823424
mov ebx,-423
imul ebx ; EDX:EAX = FFFFFFFF86635D80h, OF=0
OF=0 because EDX is a sign extension of EAX.

## Slide 9: Your turn . . .
mov ax,8760h
mov bx,100h
imul bx
What will be the hexadecimal values of DX, AX, and the Carry flag after the following instructions execute?
DX = FF87h, AX = 6000h, OF = 1

## Slide 10: Two-Operand Form for IMUL
Contrary to MUL, the IMUL instruction can be used with two operands:
    IMUL destination,source
The source operand can be imm, mem, or reg. But the destination must be a 16-bit or 32-bit register.
The product is stored (only) into the destination operand. No other registers are changed. Ex:
    MOV eax,1 ;eax = 00000001h
    IMUL ax,-1 ;eax = 0000FFFFh, CF=OF=0
    MOV eax,100h ;eax = 28 = 256
    IMUL ax,100h ;eax = 00010000h, CF=OF=1
    MOV eax,100h
    IMUL eax,100h ;eax = 00010000h, CF=OF=0
    ;For two-op IMUL: CF=OF=1 if Destination cannot contain Result

## Slide 11: Examples of MUL and IMUL
Say that AX = 1h and BX = FFFFh, then:
  Instruction Result DX AX CF/OF
  mul bx 65535 0000 FFFF 0
  imul bx -1 FFFF FFFF 0
Say that AX = FFFFh and BX = FFFFh, then:
  Instruction Result DX AX CF/OF
  mul bx 4294836225 FFFE 0001 1
  imul bx 1 0000 0001 0

## Slide 12: Examples of MUL and IMUL (cont.)
AL = 30h and BL = 4h, then:
  Instruction Result AH AL CF/OF
  mul bl 192 00 C0 0
  imul bl 192 00 C0 1
AL = 80h and BL = FFh, then
  Instruction Result AH AL CF/OF
  mul bl 32640 7F 80 1
  imul bl 128 00 80 1

## Slide 13: Exercise 1
Give the hexadecimal content of AX and the values of CF and OF immediately after the execution of each instruction below
  IMUL AH ;when AX = 0FE02h
  MUL BH ;when AL = 8Eh and BH = 10h
  IMUL BH ;when AL = 9Dh and BH = 10h
  IMUL AX,0FFh ;when AX = 0FFh

## Slide 14: Integer Division
Notation for integer division:
  Ex: 7 ¸ 2 = (3, 1) not_equal to 7 / 2 = 3.5
  dividend ¸ divisor = (quotient, remainder)
We have 2 instructions for division:
  DIV divisor ;unsigned division
  IDIV divisor ;signed division
The divisor must be reg or mem
Convention for IDIV: the remainder has always the same sign as the dividend.
  Ex: -5 ¸ 2 = (-2, -1) ; not: (-2, 1)

## Slide 15: DIV Instruction
The DIV (unsigned divide) instruction performs 8-bit, 16-bit, and 32-bit division on unsigned integers
A single operand is supplied (register or memory operand), which is assumed to be the divisor
Instruction formats:
    DIV reg/mem8
    DIV reg/mem16
    DIV reg/mem32
Dividend is always twice larger than Divisor
Default Operands:

## Slide 16: DIV Examples
Divide 8003h by 100h, using 16-bit operands:
mov dx,0 ; clear dividend, high
mov ax,8003h ; dividend, low
mov cx,100h ; divisor
div cx ; AX = 0080h, DX = 3
Same division, using 32-bit operands:
mov edx,0 ; clear dividend, high
mov eax,8003h ; dividend, low
mov ecx,100h ; divisor
div ecx ; EAX = 00000080h, DX = 3
  We have a divide overflow whenever the quotient cannot be contained in its destination (e.g., AL if divisor is byte...): execution then traps into the OS which displays a message on screen and terminates the program

## Slide 17: Your turn . . .
mov dx,0087h
mov ax,6000h
mov bx,100h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = 0000h, AX = 8760h

## Slide 18: Your turn . . .
mov dx,0087h
mov ax,6002h
mov bx,10h
div bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
Divide Overflow

## Slide 19: Signed Integer Division (IDIV)
Signed integers must be sign-extended before division takes place
  fill high byte/word/doubleword with a copy of the low byte/word/doubleword's sign bit
For example, the high byte contains a copy of the sign bit from the low byte:

## Slide 20: CBW, CWD, CDQ Instructions
The CBW, CWD, and CDQ instructions provide important sign-extension operations:
  CBW (convert byte to word) extends AL into AH
  CWD (convert word to doubleword) extends AX into DX
  CDQ (convert doubleword to quadword) extends EAX into EDX
Example:
    .data
    dwordVal SDWORD -101 ; FFFFFF9Bh
    .code
    mov eax,dwordVal
    cdq ; EDX:EAX = FFFFFFFFFFFFFF9Bh

## Slide 21: IDIV Instruction
IDIV (signed divide) performs signed integer division
Same syntax and operands as DIV instruction
Example: 8-bit division of –48 by 5
mov al,-48
cbw ; extend AL into AH
mov bl,5
idiv bl ; AL = -9, AH = -3

## Slide 22: IDIV Examples
Example: 32-bit division of –48 by 5
mov eax,-48
cdq ; extend EAX into EDX
mov ebx,5
idiv ebx ; EAX = -9, EDX = -3
Example: 16-bit division of –48 by 5
mov ax,-48
cwd ; extend AX into DX
mov bx,5
idiv bx ; AX = -9, DX = -3

## Slide 23: Your turn . . .
mov ax,0FDFFh ; -513
cwd
mov bx,100h
idiv bx
What will be the hexadecimal values of DX and AX after the following instructions execute? Or, if divide overflow occurs, you can indicate that as your answer:
DX = FFFFh (-1), AX = FFFEh (-2)

## Slide 24: Examples of DIV and IDIV
DX = 0000h, AX = 0005h, BX = FFFEh:
  Instruction Quot. Rem. AX DX
  div bx 0 5 0000 0005
  idiv bx -2 1 FFFE 0001
DX = FFFFh, AX = FFFBh, BX = 0002h:
  Instruction Quot. Rem. AX DX
  idiv bx -2 -1 FFFE FFFF
  div bx Divide Overflow

## Slide 25: Examples of DIV and IDIV (cont.)
AX = 0007, BX = FFFEh:
  Instruction Quot. Rem. AL AH
  div bl 0 7 00 07
  idiv bl -3 1 FD 01
AX = 00FBh, BX = 0CFFh:
  Instruction Quot. Rem. AL AH
  div bl 0 251 00 FB
  idiv bl Divide Overflow

## Slide 26: Exercise 2
Give the hexadecimal content of AX immediately after the execution of each instruction below or indicate if there is a divide overflow
  IDIV BL ; when AX = 0FFFBh and BL = 0FEh
  IDIV BL ; when AX = 0080h and BL = 0FFh
  DIV BL ; when AX = 7FFFh and BL = 08h

## Slide 27: Preparing for a division
Recall that:
  For a byte divisor: the dividend is in AX
  For a word divisor: the dividend is in DX:AX
  For a dword divisor: the dividend is in EDX:EAX
If the dividend occupies only its least significant half (lsh) we must prepare its most significant half (msh) for a division
  For DIV: the msh must be zero
  For IDIV: the msh must be the sign extension of the lsh

## Slide 28: Preparing for DIV or IDIV
To divide the unsigned number in AX by the unsigned number in BX, you must do
    xor dx,dx ;or mov dx, 0 to fill DX with 0
    div bx
To divide the signed number in AX by the signed number in BX, you must do
    cwd ;to fill DX with sign extension of AX
    idiv bx
Never assign the msh of the dividend to zero before performing IDIV

## Slide 29: Unsigned Arithmetic Expressions
Some good reasons to learn how to implement integer expressions:
  Learn how do compilers do it
  Test your understanding of MUL, IMUL, DIV, IDIV
  Check for overflow (Carry and Overflow flags)
Example: var4 = (var1 + var2) * var3
; Assume unsigned operands
mov eax,var1
add eax,var2 ; EAX = var1 + var2
mul var3 ; EAX = EAX * var3
jc TooBig ; check for carry
mov var4,eax ; save product

## Slide 30: Signed Arithmetic Expressions (1 of 2)
Example: eax = (-var1 * var2) + var3
mov eax,var1
neg eax
imul var2
jo TooBig ; check for overflow
add eax,var3
jo TooBig ; check for overflow
Example: var4 = (var1 * 5) / (var2 – 3)
mov eax,var1 ; left side
mov ebx,5
imul ebx ; EDX:EAX = product
mov ebx,var2 ; right side
sub ebx,3
idiv ebx ; EAX = quotient
mov var4,eax

## Slide 31: Signed Arithmetic Expressions (2 of 2)
Example: var4 = (var1 * -5) / (-var2 % var3);
mov eax,var2 ; begin right side
neg eax
cdq ; sign-extend dividend
idiv var3 ; EDX = remainder
mov ebx,edx ; EBX = right side
mov eax,-5 ; begin left side
imul var1 ; EDX:EAX = left side
idiv ebx ; final division
mov var4,eax ; quotient
Sometimes it's easiest to calculate the right-hand term of an expression first.

## Slide 32: Your turn . . .
mov eax,20
imul ebx
idiv ecx
Implement the following expression using signed 32-bit integers:
eax = (ebx * 20) / ecx

## Slide 33: Your turn . . .
push edx
push eax ; EAX needed later
mov eax,ecx
imul edx ; left side: EDX:EAX
pop ebx ; saved value of EAX
idiv ebx ; EAX = quotient
pop edx ; restore EDX, ECX
Implement the following expression using signed 32-bit integers. Save and restore ECX and EDX:
eax = (ecx * edx) / eax

## Slide 34: Your turn . . .
mov eax,var1
mov edx,var2
neg edx
imul edx ; left side: EDX:EAX
mov ecx,var3
sub ecx,ebx
idiv ecx ; EAX = quotient
mov var3,eax
Skip to Page 54
Implement the following expression using signed 32-bit integers. Do not modify any variables other than var3:
var3 = (var1 * -var2) / (var3 – ebx)

## Slide 35: Binary-Coded Decimal
Binary-coded decimal (BCD) integers use 4 binary bits to represent each decimal digit
A number using unpacked BCD representation stores a decimal digit in the lower four bits of each byte
  For example, 5,678 is stored as the following sequence of hexadecimal bytes:
  Stored in binary as:
    0000 0101 0000 0110 0000 0111 0000 1000
05
06
07
08h

## Slide 36: ASCII Decimal
A number using ASCII Decimal representation stores a single ASCII digit in each byte
  For example, 5,678 is stored as the following sequence of hexadecimal bytes:
  Stored in binary as:
    0011 0101 0011 0110 0011 0111 0011 1000
35
36
37
38h

## Slide 37: AAA Instruction
The AAA (ASCII adjust after addition) instruction adjusts the binary result of an ADD or ADC instruction. It makes the result in AL consistent with ASCII decimal representation.
  The Carry value, if any ends up in AH
Example: Add '8' and '2'
mov ah,0
mov al,'8' ; AX = 0038h
add al,'2' ; AX = 006Ah
aaa ; AX = 0100h (adjust result)
or ax,3030h ; AX = 3130h = '10'

## Slide 38: AAS Instruction
The AAS (ASCII adjust after subtraction) instruction adjusts the binary result of an SUB or SBB instruction. It makes the result in AL consistent with ASCII decimal representation.
  It places the Carry value, if any, in AH
Example: Subtract '9' from '8'
mov ah,0
mov al,'8' ; AX = 0038h
sub al,'9' ; AX = 00FFh
aas ; AX = FF09h, CF=1
or al,30h ; AL = '9'

## Slide 39: AAM Instruction
The AAM (ASCII adjust after multiplication) instruction adjusts the binary result of a MUL instruction. The multiplication must have been performed on unpacked BCD numbers.
mov bl,05h ; first operand
mov al,06h ; second operand
mul bl ; AX = 001Eh
aam ; AX = 0300h

## Slide 40: AAD Instruction
The AAD (ASCII adjust before division) instruction adjusts the unpacked BCD dividend in AX before a division operation
.data
quotient BYTE ?
remainder BYTE ?
.code
mov ax,0307h ; dividend
aad ; AX = 0025h
mov bl,5 ; divisor
div bl ; AX = 0207h
mov quotient,al
mov remainder,ah

## Slide 41: Packed Decimal Arithmetic
Packed decimal integers store two decimal digits per byte
  For example, 12,345,678 can be stored as the following sequence of hexadecimal bytes:
12
34
56
78h
Packed decimal is also known as packed BCD.
Good for financial values – extended precision possible, without rounding errors.

## Slide 42: DAA Instruction
The DAA (decimal adjust after addition) instruction converts the binary result of an ADD or ADC operation to packed decimal format.
  The value to be adjusted must be in AL
  If the lower digit is adjusted, the Auxiliary Carry flag is set.
  If the upper digit is adjusted, the Carry flag is set.

## Slide 43: DAA Logic
If (AL(lo) > 9) or (AuxCarry = 1)
AL = AL + 6
AuxCarry = 1
Else
AuxCarry = 0
Endif
If (AL(hi) > 9) or Carry = 1
AL = AL + 60h
Carry = 1
Else
Carry = 0
Endif
If AL = AL + 6 sets the Carry flag, its value is used when evaluating AL(hi).

## Slide 44: DAA Examples
Example: calculate BCD 35 + 48
mov al,35h
add al,48h ; AL = 7Dh
daa ; AL = 83h, CF = 0
Example: calculate BCD 35 + 65
mov al,35h
add al,65h ; AL = 9Ah
daa ; AL = 00h, CF = 1
Example: calculate BCD 69 + 29
mov al,69h
add al,29h ; AL = 92h
daa ; AL = 98h, CF = 0

## Slide 45: Your turn . . .
A temporary malfunction in your computer's processor has disabled the DAA instruction. Write a procedure in assembly language that performs the same actions as DAA.
Test your procedure using the values from the previous slide.

## Slide 46: DAS Instruction
The DAS (decimal adjust after subtraction) instruction converts the binary result of a SUB or SBB operation to packed decimal format.
The value must be in AL
Example: subtract BCD 48 from 85
mov al,48h
sub al,35h ; AL = 13h
das ; AL = 13h CF = 0

## Slide 47: DAS Logic
If (AL(lo) > 9) OR (AuxCarry = 1)
AL = AL − 6;
AuxCarry = 1;
Else
  AuxCarry = 0;
Endif
If (AL > 9FH) or (Carry = 1)
AL = AL − 60h;
Carry = 1;
Else
Carry = 0;
Endif
If AL = AL - 6 sets the Carry flag, its value is used when evaluating AL in the second IF statement.

## Slide 48: DAS Examples (1 of 2)
Example: subtract BCD 48 – 35
mov al,48h
sub al,35h ; AL = 13h
das ; AL = 13h CF = 0
Example: subtract BCD 62 – 35
mov al,62h
sub al,35h ; AL = 2Dh, CF = 0
das ; AL = 27h, CF = 0
Example: subtract BCD 32 – 29
mov al,32h
add al,29h ; AL = 09h, CF = 0
daa ; AL = 03h, CF = 0

## Slide 49: DAS Examples (2 of 2)
Example: subtract BCD 32 – 39
mov al,32h
sub al,39h ; AL = F9h, CF = 1
das ; AL = 93h, CF = 1
Steps:
AL = F9h
CF = 1, so subtract 6 from F9h
AL = F3h
F3h > 9Fh, so subtract 60h from F3h
AL = 93h, CF = 1

## Slide 50: Your turn . . .
A temporary malfunction in your computer's processor has disabled the DAS instruction. Write a procedure in assembly language that performs the same actions as DAS.
Test your procedure using the values from the previous two slides.

## Slide 51: The XLAT instruction
The XLAT instruction (without any operands) is the basic tool for character translation.
Upon execution of XLAT:
  The byte pointed by EBX + AL is moved to AL
    .data
    table BYTE ‘0123456789ABCDEF’
    .code
    mov ebx, offset table
    mov al, 0Ah
    xlat ;AL = ‘A’ = 41h
    ;converts from binary to ASCII code of
    ;hex digit

## Slide 52: Character Encoding
This is a table to encode numerical and alphabetical characters:
.data
codetable label byte
BYTE 48 dup(0) ; no translation
BYTE '4590821367' ; ASCII codes 48-57
BYTE 7 dup (0) ; no translation
BYTE 'GVHZUSOBMIKPJCADLFTYEQNWXR'
BYTE 6 dup (0) ; no translation
BYTE 'gvhzusobmikpjcadlftyeqnwxr'
BYTE 133 dup(0) ; no translation

## Slide 53
mov ebx,offset codetable
nextchar:
call ReadChar ; char in AL
mov dl,al ; save original in DL
xlat ; translate char in AL
cmp al,0 ; not translatable?
je putOriginal ; then write original char
call WriteChar ; else, write translation
jmp nextchar
putOriginal:
mov al,dl
call WriteChar
jmp nextchar
Character Encoding (cont.)
This is a code snippet to encode (only) numerical and alphabetical characters:

## Slide 54: Binary to ASCII Conversion
We want to convert a binary number into the string of ASCII digits that represents its unsigned value (for display).
Ex: if AX = 4096, to generate the string “4096” we divide by 10 until the quotient is 0:
  [the same method can be used to obtain the ASCII string of digits with respect to any bases]
Dividend / 10 = Quotient Remainder
/ 10 = 409 6
409 / 10 = 40 9
40 / 10 = 4 0
4 / 10 = 0 4
ASCII String: 4 0 9 6

## Slide 55: Binary to ASCII Conversion (cont.)
The same method can be used to obtain the ASCII string of digits with respect to any base
Ex: if AX = 10C4h = 4292, to generate the string “10C4” we divide by 16 until the quotient is 0:
Dividend / 16 = Quotient Remainder
4292 / 16 = 268 4
268 / 16 = 16 12
16 / 16 = 1 0
1 / 16 = 0 1
ASCII String: 1 0 C 4

## Slide 56: Binary to ASCII Conversion (cont.) [skip]
Write the Wuint program which displays the ASCII string of the unsigned value in EAX
  EBX contains a radix value (2 to 16) that determines the base of the displayed number
Write the Wsint program which displays the ASCII string of the signed value in EAX:
  Check the sign bit. If the value is negative, perform two’s complement (with the NEG instruction) and display “-”
  Then use the same algorithm, Wuint, to display the digits of the (now) positive number

## Slide 57: ASCII to Binary Conversion
To convert a sequence of ASCII digits into its numerical value:
  for each new digit, we multiply by the base and add the new digit.
Ex: to convert “4096” into its base-10 value:
Value
Before
New
Digit
Value
After
0 x 10 + 4 = 4
4 x 10 + 0 = 40
40 x 10 + 9 = 409
409 x 10 + 6 = 4096
Final value

## Slide 58: ASCII to Binary Conversion (cont.) [skip]
Write the Rint program which reads a string of ASCII decimal digits and stores the base 10 numerical value into EAX
  For signed numbers: the sequence of digits can be preceded by a sign.
  Checks for overflows at each multiplication and addition
The side program uses both Rint and Wsint
INCLUDE Irvine32.inc
.data
msg1 BYTE “Enter an int: “,0
msg2 BYTE “EAX = “,0
.code
main PROC
mov edx,OFFSET msg1
Call WriteString
call Rint
mov edx,OFFSET msg2
Call WriteString
mov ebx,10 ; base 10
call Wsint
exit ; from main
main ENDP
include Wsint.asm
include Rint.asm
END main